## Hexbot Script Compiler

#### Introduction

This document is a description of one possible design for a compiler that simplifies the creation and processing of scripts that describe leg movements of the Hexbot robot. This is an early draft, and is subject to major revision or rejection.

#### Goals
1. reduce the amount of effort needed to create the scripts that define robot movements known as flows
2. speed up the development of movement scripts, which is currently labour intensive.
3. shift the mathematical calculations to the compiler
4. to provide feedback on errors or dangerous behaviour in scripts
5. allow the flow designer to work in higher level operations, such as “move the robot 3 cm forward” or “tilt 10 degrees to the left” rather than numeric coordinates for toes
6. provide plug in points for other related functionality such as script validation, visualization, simulation
7. provide a way to embed flows in the robot source code

#### Risks

1. Complex math required to produce output script will be difficult to debug
2. Incorrect numeric output may go undetected
3. dependence on MQTT.fx and its file format

#### Implementation Constraints

This utility needs to run in the Windows and Mac environments, on the same platforms that run MQTT.fx. To achieve portability, it will be written in C Sharp and developed within the Microsoft Visual Studio Code framework which is currently used for the robot software environment.
#### Overview

This diagram describes the role of the compiler and the related utilities and files that are currently foreseen.

Generic text editor	A simple editor for unformatted text such as Notepad++, or VSC editor
Movement Source File	The file containing commands to the compiler, one per line
Symbol Definitions file	A simple text file containing definitions for symbols of the form $A. Direct symbol substitutions are done in the template and script file processing. Reserved symbols are used for the hexbot name, script file name and MQTT .JS file name ( $H, $I and $O) (and maybe $F for feature enables?)
Movement compiler	The C++ program that processes the movement source file and creates an equivalent MQTT.fx script file, and a list or errors and warnings
MQTT.fx script file	A standard, complete MQTT.fx script file that can be downloaded to a robot without further processing
Error and Warning Listing	A list of exception detected by the compiler
Validation and performance analysis	Future software that will analyze a script to detect inappropriate behaviour or measure the expected performance
MQTT.fx	The existing MQTT.fx client software
Visualization and simulation	Future software produces a graphical display of a script’s results
Script reformatter	Software that translates the script produced by the compiler into a format that allows it to be embedded in the robot source code
Execution in robot	The result of using MQTT.fx to download the compiled script into the robot, and execute it
Embeddable robot C++ code	A version of the script that can be added to the robot source so it can be executed immediately without downloading via MQTT.fx.

#### Command Set

Commands are at the beginning of the line and are terminated by a space character
Commands and arguments are not case sensitive. Greyed out commands are not implemented yet.

//	Comment that is passed through to script
Leggroup a,1,2,3	Define a group of legs, represented by a letter, that all get the same commands. See Leg Group section of this document.
Tilt bearing, degrees	Defines a tilt for robot to achieve. / - Bearing is a number from 0 – 359, 0 means straight forward, 90 means to the robot’s right... / - degrees is the tilt from vertical. 1 degree is a slight tilt towards the bearing
Tiltinc BearingInc, DegreesInc, count	Defines a tilt for robot to achieve. / - Bearing is a number from 0 – 359 representing the adjustment to the bearing made on each doit command / - DegreeInc is the adjustment added to the tile on each doit command / - count is the number of doit commands to repeat this command over
MoveToHomePosition	Move all legs to their home position. No need for a following Doit command, since a “Doit 500” is built into this command.
MoveAbsoluteGlobal leg, x, y, z	Prepare to move leg (which can be a leg number or a leggroup) to the absolute global coordinates x, y and z.
MoveAbsoluteLocal leg, x, y, z	Prepare to move leg (which can be a leg number or a leggroup) to the local coordinates x, y and z.
MoveRelHomeGlobal leg, x, y, z, count	Prepare to move leg (which can be a leg number or a leggroup) to the location which is the home position adjusted by x in the GLOBAL x direction, by y in the GLOBAL y direction and by z in the GLOBAL z direction.
MoveRelHomeLocal leg, x, y, z, count	Prepare to move leg (which can be a leg number or a leg group) to the location which is the home position adjusted by x in the LOCAL x direction, by y in the LOCAL y direction and by z in the LOCAL z direction. Do this for each of the next “count” doit commands. Count defaults to 1
MoveRelLastGlobal leg, x, y, z, count	Prepare to move leg (which can be a leg number or a leg group) to the location which is the LAST position for the leg adjusted by x in the GLOBAL x direction, by y in the GLOBAL y direction and by z in the GLOBAL z direction. Do this for each of the next “count” doit commands. Count defaults to 1
MoveRelLastLocal leg, x, y, z, count	Prepare to move leg (which can be a leg number or a leggroup) to the location which is the LAST position for the leg adjusted by x in the LOCAL x direction, by y in the LOCAL y direction and by z in the LOCAL z direction. Do this for each of the next “count” doit commands. Count defaults to 1
Rotate leg, degrees, count	Prepare to move leg (which can be a leg number or a leggroup) by rotating it through “degrees” maintaining its radius from robot’s center, global (0,0,*). Do this for each of the next “count” doit commands. Count defaults to 1
VerticalDisplace cm, count	Move center of robot up or down by cm centimeters. (up and down by changing global Z coordinate, not along tilt axis.) Do this for each of the next “count” doit commands. Count defaults to 1
Pause	Prepare to have the robot pause in place for the time given in the next doit command. (or maybe until an MQTT command or a button push?)
Doit msec	Calculate all the move, tilt, and vertical displacement changes to toe positions, and write out the appropriate command to the output file.
SetOutputOperation	Tell the compiler what operation parameter should be used in the flow commands it outputs to the file. This will affect the numbers that are output as well.
CycleStart name	Indicate the beginning of a named subsection of the flow that will be repeated via an ExecuteCycle command later
CycleEnd name	Indicate the end of a named subsection of the flow that will be repeated via an ExecuteCycle command later
ExecuteCycle name, count	Repeat a named subsection of the flow for a number of repetitions
End	Indicates the end of the source file

#### Symbols
Symbolic names in the form of a single letter can be used to represent arbitrary text strings in the template and script files. Symbols are defined in the file “symbols.txt” which is specific to the computer it appears on, and is not tracked by Git. This allows it to define unique local information such as the identifier for the hexbot, or the file path for the compiled output. Since the templates and scripts contain the name of the symbol rather than the specific local information, they can be shared and tracked by Git.

Symbols can also be used to parameterize some attribute of a script. For example, the best step length for a walking gait might not be know when the script is initially written. By using $S for the step length in the script, multiple values can be tested by changing the value of $S in the symbols.txt file, and recompiling. Otherwise, every occurrence of of the step size in the script would need to be edited for every test.

Symbol names consist of a single letter of the alphabet, and are not case sensitive. By convention, symbols are specified and referenced in upper case, to distinguish them from features, which are lower case letters.

Symbols are defined by including a line in symbols.txt that contains:
- the letter name of the symbol, as the first character on a line
- a single space character
- the text string that the symbol represents.

The text string may contain almost any text, including upper and lower case, spaces, and special characters. It may not include newline characters.

If a symbols is defined more than once, that latest definition will supersede the previous one(s).

There are some reserved symbols that are used to convey information to the compler, functioning like .INI files in Windows. These are:

$H The Hexbot identifier, used in MQTT messages
$I The name of the input script file, preceded by an optional path
$O The name of the output MQTT file, preceded by an optional path.

If these values are defined in the symbols.txt file, the compiler will read and use them, rather than asking the user to provide them at compile time. In this case, a message is displayed indicating what value is being used.

Lines in the symbols file that are blank, or start with a forward slash or space character will be treated as comments and ignored.

Examples of symbol files, and other files are in another section of this document.

#### Leg Groups
The compiler commands that control the robot’s leg activity typically start with the word “Move” such as “MoveRelLastLocal“, which is described in the Command Set section. These move commands reference a particular leg, and specify a movement pattern for that leg. Sometimes the same movement pattern needs to be done for multiple legs, and leg groups simplify coding this repetition in the script file.

A leg group is simply some combination of legs, represented by a name which is a single letter. The LegGroup command is used to define a leg group. It looks like this:
      LegGroup w, 1, 3, 5

which means: define the leg group with the name “w” to consist of legs 1, 3, and 5.

Leg group names are case insensitive, but by convention, lower case is used. Symbols also use case insensitive single letters as names, but there is no conflict and the same letter can be used for both a symbol and leg group. Upper case is the convention for symbol names. Leg groups must be defined before they are used in a script.

Move commands that reference a leg, can use a number to specify a single leg, or a letter to specify the name of a leg group. If a leg group name is given, the command is executed for all legs that are part of the group. For example, if the Leg Group definition above has been done, the command:
     MoveRelLastLocal w, 0, 4, 0

would be equivalent to:
     MoveRelLastLocal 1, 0, 4, 0
     MoveRelLastLocal 3, 0, 4, 0
     MoveRelLastLocal 5, 0, 4, 0

Frequently used leg combinations are predefined in the compiler. They can be overwritten with a new definition, but a compiler warning will be generated. These leg groups are:

   a - all - 1,2,3,4,5,6
  b – back - 3,6
  f - front - 1,4
  l - left - 4,5,6
  r – right - 1,2,3
  o - odds - 1,3,5
  e – evens - 2,4,6
  m - middles - 2,5

It is possible to use a symbol, which is also a letter (usually upper case) to represent the leg number, or leg group, that will be used in a move command. However, in this case the letter will be preceded by a “$” character, which defines the following character as a symbol name, and causes symbol substitution to occur.

For example, if your symbols.txt file contains the line
    X w

and your script contains the lines
    LegGroup w, 1, 3, 5
    MoveRelLastLocal $X, 3, 4, 0

The move command will look like this after symbol substitution:
    MoveRelLastLocal w, 3, 4, 0

and will execute like this:
    MoveRelLastLocal 1, 3, 4, 0
    MoveRelLastLocal 3, 3, 4, 0
    MoveRelLastLocal 5, 3, 4, 0
#### Example Files
Compilation Run

PS C: hexbotMQTTScriptCompiler-> dotnet run

  (using predefined script file name: scripts\test-from-folder.txt)
  (using predefined Robot name: Hexbot3C61054ADD9)
  (using predefined output MQTT file name: C:\Users\DougElliott\AppData\Local\MQTT-FX\scripts\01__hb-test-from-folder.js)
--- Compilation was successful with no warnings or errors ---

symbols.txt

/ This is the file symbols.txt which resides in the hexbotMQTTScriptCompiler- folder
/ Documentation: doc/compiler-spec.odt , section titled Symbols
/ File format:
/ blank lines, or lines starting with "/" are considered to be comments and are ignored
/ symbol definition lines consist of:
/ a letter in column 1 (case insensitive) representing the name of the symbol
/ a single space character
/ the text string associated with the symbol, which may contain spaces and special characters
/ a final newline character
/ Reserved symbols, used by the compiler for specific purposes
/ $H The Hexbot identifier, used in MQTT messages
/ $I The name of the input script file, preceded by an optional path
/ $O The name of the output MQTT file, preceded by an optional path.
/ $F Reserved for future use to enable individual features at compile time
/ see the documentation file referenced above for examples.

/ H is the name of the robot, for MQTT purposes
/ Andrew: Hexbot94B97E5F4A40
/ Doug: Hexbot3C61054ADD98
H Hexbot3C61054ADD9

/ input file location, including relative path
I scripts\test-from-folder.txt

/ output file location, including absolute path
O C:\Users\DougElliott\AppData\Local\MQTT-FX\scripts\01__hb-test-from-folder.js

/ parameterized leg number that will be tested by resulting js code
L 5

/ number of test cycles to repeat (plus the initial one)
C 4

/ time interval in milliseconds for each leg movement
T 600

template.txt

copy var Thread = Java.type("java.lang.Thread");
copy function execute() {
copy mybot = "$H/commands"
copy send("NEW_FLOW")
insert <templateFile>
copy send("DO_FLOW,49,50")
copy action.setExitCode(0);
copy action.setResultText("done.");
copy out("Parameter parameter set up complete");
copy return action;
copy }
copy function send(cmd){
copy out(cmd); // display command in MQTT console as its downloaded to bot
copy mqttManager.publish(mybot, cmd);
copy Thread.sleep(200);
copy }
copy function out(message){
copy output.print(message);
copy }
Input Script File

PS C: hexbotMQTTScriptCompiler-> type .\scripts\test-from-folder.txt

MoveToHomePosition
LegGroup x,1,6
CycleStart 1
MoveRelLastLocal $L, 0, 4, 0,
Doit $T
MoveRelLastLocal $l, 4, 0, 0,
Doit $T
MoveRelLastLocal $L, -4, 0, 0,
Doit $T
MoveRelLastLocal $L, 0, -4, 0,
Doit $T
MoveRelLastGlobal a,2,-3,5
MoveRelLastLocal x,0,2,0
Doit $T
CycleEnd 1
ExecuteCycle 1,$C

MQTT .JS Output File

// ****************************************************************************************************
// This MQTTfx script for Hexbot robot created by hexbotScriptCompiler on 4/28/2022 at 18:35:42.2892525
// NOTE: Doug's robot = Hexbot3C61054ADD98, Andrew's robot = Hexbot94B97E5F4A40.
// ****************************************************************************************************
var Thread = Java.type("java.lang.Thread");
function execute() {
mybot = "Hexbot3C61054ADD9/commands"
send("NEW_FLOW")
send("Flow, 1,MLRH,10,0,0,0, 0,0,0, 0,0,0, 0,0,0, 0,0,0, 0,0,0, 0,0,0")
send("Flow,500,MLC,10,0,0,0 ,13.78,-10.6,0 ,13.78,-10.6,0 ,13.78,-10.6,0 ,13.78,-10.6,0 ,13.78,-10.6,0 ,13.78,-10.6,0")
send("Flow,0,MCS,1,0,0,0")
send("Flow,600,MLC,10,0,0,0 ,13.78,-10.6,0 ,13.78,-10.6,0 ,13.78,-10.6,0 ,13.78,-10.6,0 ,13.78,-6.6,0 ,13.78,-10.6,0")
send("Flow,600,MLC,10,0,0,0 ,13.78,-10.6,0 ,13.78,-10.6,0 ,13.78,-10.6,0 ,13.78,-10.6,0 ,17.78,-6.6,0 ,13.78,-10.6,0")
send("Flow,600,MLC,10,0,0,0 ,13.78,-10.6,0 ,13.78,-10.6,0 ,13.78,-10.6,0 ,13.78,-10.6,0 ,13.78,-6.6,0 ,13.78,-10.6,0")
send("Flow,600,MLC,10,0,0,0 ,13.78,-10.6,0 ,13.78,-10.6,0 ,13.78,-10.6,0 ,13.78,-10.6,0 ,13.78,-10.6,0 ,13.78,-10.6,0")
send("Flow,600,MLC,10,0,0,0 ,17.32,-3.6,-0.71 ,16.78,-5.6,2 ,27.03,-5.6,3.54 ,-0.09,-5.6,9.63 ,10.78,-5.6,-2 ,10.24,-3.6,0.7")
send("Flow,0,MCE,1,0,0,0")
send("Flow,0,DC,1,4,0,0,0")
send("DO_FLOW,49,50")
action.setExitCode(0);
action.setResultText("done.");
out("Parameter parameter set up complete");
return action;
}
function send(cmd){
out(cmd); // display command in MQTT console as its downloaded to bot
mqttManager.publish(mybot, cmd);
Thread.sleep(200);
}
function out(message){
output.print(message);
}
#### Error Messages
There are now routines for generating and storing one line messages for warnings and errors detected, and these are displayed at the end of the compilation. The way to display a message is to make a call like this:
        newError(lineNum, "type-string","message-string")
where:
- lineNum is a line number within the symbols, template or script file, for reference
- "type-string" is either "Error:" or "Warning:"
- "message-string" is a descriptive message identifying the cause of the message

If no warnings or errors are generated, this message is displayed at the end of the compilation:
--- Compilation was successful with no warnings or errors ---
Since the symbols.txt file is processed in both the template and script objects, only the template version reported symbol errors. The line numbers for these are within the symbols.txt file, and the message starts with "In symbols.txt: ". As a result of this structure, symbol file errors are listed as template errors.
Here's an example of a compilation with lots of errors:
PS C: hexbotMQTTScriptCompiler-> dotnet run

  (using predefined script file name: scripts\test-from-folder.txt)
  (using predefined Robot name: Hexbot3C61054ADD98)
  (using predefined output MQTT file name: C:\Users\DougElliott\AppData\Local\MQTT-FX\scripts\01__hb-test-from-folder.js)
--- Errors in Template file --
  Line 36 Error: In symbols.txt file: Symbol name at start of line is not a single letter
  Line 37 Error: In symbols.txt: line too short or missing space separator
  Line 37 Error: In symbols.txt file: Symbol name at start of line is not a single letter
  Line 3 Warning: Replace command is deprecated. Consider a copy command that references $H
--- Errors in Script file ---
  Line 1 Warning: symdef command is obsolete, replaced by symbols in the symbol.txt file
  Line 18 Error: Unknown command in script src file: bad-command

PS C: hexbotMQTTScriptCompiler->

and one with no errors or warnings:
PS C: hexbotMQTTScriptCompiler-> dotnet run

  (using predefined script file name: scripts\test-from-folder.txt)
  (using predefined Robot name: Hexbot3C61054ADD9)
  (using predefined output MQTT file name: C:\Users\DougElliott\AppData\Local\MQTT-FX\scripts\01__hb-test-from-folder.js)
--- Compilation was successful with no warnings or errors ---

PS C: hexbotMQTTScriptCompiler->
To generate a crude but useful list of all error messages and warnings generated by the compiler, run the following linux command to scan the Program.cs source file (the space counts are important):

      egrep ' newEr|ic class' Program.cs|sed 's/^ */ /g'|sed 's/^ p/\np/g'

which gives output like this:

$ egrep ' newEr|ic class' Program.cs|sed 's/^ */ /g'|sed 's/^ p/\np/g'

public class templateFile
     newError(symLine, "Error:", "In symbols.txt file: Symbol name at start of line is not a single letter");
     newError(symLine,"Warning:", "In symbols.txt file: substitution string was empty");
     newError(lineNum,"Warning:", "Replace command is deprecated. Consider a copy command that references $H" );

public class scriptFile
     newError(symLine, "Error:", "In symbols.txt: line too short or missing space separator");
     newError(lineNum,"Warning:", "symdef command is obsolete, replaced by symbols in the symbol.txt file");
     newError(lineNum, "Error:", "Doit command did not have mandatory time duration argument");
     newError(lineNum,"Warning:",$"LegGroup definition overwrote a previous definition for group {legName}");
     newError(lineNum, "Error:", "Unknown command in script source file: " + cmd);

#### Implementation Notes
-idea of spreading an action over a bunch of commands, like:
     - change tilt bearing by -10 degrees for each of next 18 doit commands
     - move forward 1 cm on each of next 10 doit commands
- move forward a total of 12 cm, spread over the next 8 doit commands
-handy output for script development, like: - output position of leg 1’s toe in local coordinates until further notice
- control what goes in output listing
     - all source lines, plus errors or warning lines
     - generated toes positions in some format (carefully formatted for readability)
     - display how close each toes gets to safety box (which we’d have to define somehow)
     - display how close each toes gets to hitting part of chassis
     - or only display above 2 bits of info if danger distance is less than some criteria
- output listing to file, or to console
-maybe define higher level macros that consists of multiple move commands such as:
- STEP(direction, gait, stride)
- ROTATE( direction, angle increment)
- ...
- command to repeat last flow that was downloaded. It’s already sitting in memory, and doesn’t need to be reloaded, just restarted, possibly with some re-initialization.

#### Data Structures

The compiler needs to track the following data in order to be able to operate:

Current toe positions as move commands are accumulated up to a Doit command. These are kept in both local and global coordinates:

srcLines[200] // contains a copy of input file (template or script) in template and script classes
outLines[200] // contains the output resulting when the srcLines are compiled

LegGloX[leg] // position in global coordinates
LegGloY[leg]
LegGloZ[leg]

LegLocX[leg] // position in local coordinates
LegLocY[leg]
LegLocZ[leg]

symNames[20] //defined symbols. If $X = “some-string” is defined as 4th symbol, symNames[3] = “X”
symStrings[20] // in above example, symStrings[3] would be “some-string”

#### Methodologies
Support routines
- translate global coords to local
- translate local coords to global
- 2D vector rotation?
- leg group lookup

Order of Operations
- treat pause as a special case – set a flag, & generate error on any movement commands
- init NewPosnGlobal to LastPosnGlobal after doit done
- update NewPosnGlobal as move commands are encountered
- save details of rotate, vertical, tilt commands until doit
- need persistent data (over doit commands) for any command with a count parameter
    - parameter change ( tilt bearinginc & tiltinc, vertical displace, rotation
    - iterations remaining counter
-when doit encontered
-start with moves accumulated in New Posn Global
-apply tilt (one time, or repeated)
-apply rotation (one time or repeated)
-apply vertical displace (one time or repeated)
-do safety checks for safety box, and chassis collisions
-generate output coords arrays according to appropriate operation
        -generate and output the flow command
- use a lot of flags to detect unexpected command combinations & orders, and use them to generate error
  and warning messages